ALERT
Implementation Proposal

Alert Development Team

# Targets
Implement a small-scale prototype for the theoretical proposal of ALERT [1]– An Architecture for the Emergency Retasking of Wireless Sensor Networks whose objectives are:
- Formalize the discovery and reallocation of the available capabilities in individual sensor networks.
- Provide formalism for specifying sensor missions and their attributes.
- Develop techniques for retasking independently-deployed sensor networks.

For a single mote, the user-concerned tasks and capabilities are
- What it can sense such as temperature, humidity, light, barometric pressure and seismic;
- How dose it sense such as input range, sampling frequency and resolution;
- What can it process on the data such as average, min-max, filter and signal analysis, etc.

For the whole wireless sensor network which deployed on an area of interesting, it will present the user an image of physical quantities distribution such as temperature and humidity etc. The user concerned tasks and capabilities are:
- The size, resolution, refresh rate and durability of the image determined by the number, distribution density, sampling rate and power supply of motes in the WSN;
- How many kinds of image can this WSN provides such as temperature and humidity etc;
- How does the WSN detect, predict and alarm events even emergencies happened in the area of interesting? [1]
  [1] In-network processing
- How does the WSN provide assistance to rescue team such as giving out an safe route to the victims in the AOI?
- How to handle QoS?

# Prototype
The prototype will be constructed from a subset of the equipments for the project ALERT[2]:
- 22 IRIS motes
- Sensor boards: 8 MTS 310, 2 MTS 400, 3 MTS 320, 20 MDA 100
- USB programming board: 12 MIB 520
- USB Base station/Gateway: 3 BU2110CA

Motes are IRIS backpacked with sensor boards, AFN – Aggregation and Forwarding Node can be simulated by a laptop computer plugged with a USB Base station backpacked with sensor board – MTS 420 which has GPS.

Table 1: Total Inventory from INetS at ODU-CS[2]
Equipment	Quantity	Sensors/Description
IRIS motes	12	mkelly ~ 5, inetslab ~ 2
MTS 310	8 (including Dr Olariu's 2)	Light, temperature, microphone, buzzer, 2-axis accelerometer, and 2-axis magnetometer
MTS 400	2	Light, Temperature, Humidity, Barometric Pressure and Seismic
MTS 420	3	Light, Temperature, Humidity, Barometric Pressure, Seismic and GPS
MIB 520	2	USB programming board
BU2110CA	3	USB Base Station/ Gateway
Imote2 Starter Kit	2
MIH enclosures	12
Crossbow CD	2
Ajay's Inventory
IRIS motes	10	XM2110
MIB 520	10	USB Programming board
MDA 100	20	Light, Temperature Sensor

With these equipments, an experimental pre-deployed[2] WSNs could be constructed. A sensor can be simulated by a mote piggybacked with a sensor board. The motes in the WSN could be arrayed evenly in square-like grids with side length of 1-2 meters. The WSNs has its own base-station for network management and data-collection, etc. this base-station can also act as a remote authority (command node).[3] However, due to the limited number of motes, it can only provide images of distribution of environmental physical quantities of several pixels.
[2] Where could they be deployed? In laboratory?
This WSN is pre-tasked with monitoring environmental light and temperature, data gathering every 5 seconds. Its work forces are:
- 1 USB Base Station/ Gateway: BU2110CA
- 22 IRIS motes piggybacked with MTS 310, MTS 400/420, MDA 100
- One laptop plugged the USB Base Station, show images (22 pixes corresponding to the number of motes) of light and temperature respectively.

AFN: An aggregation and forwarding node (simulate PSAR, firefighter, etc)
- 1 USB Base Station/ Gateway: BU2110CA
- One laptop plugged the USB base station.
All the motes in the WSN are preset with genetic material[1]:
- a public-domain pseudo-random number generator;
- an initial set of seeds into the random number generator;
- a set of tuples ( c_i, k(c_i) ) ( 1 le i le q) , where c_i is a color, and k(c_i ) is the secret associated with color c_i ;
- a perfect hash function that will be used for multi-tasking;
- an initial time; at this point all the clocks are synchronous; later due to clock drift, synchronization is lost.
Coordinate system setup for the WSN will be conceived on demand using some location approaches kinds of dynamic coordinate systems[3][4], GPS, location by RSSI (received signal strength indicator), etc.
The virtual infrastructure or middle ware will target on the pre-deployed WSN.
# One Working Scenario
An Emergency[3] is taking place in some area with WSNs deployed. An rescue team consists of PSAR and AFNs are deployed for handling that event.[3] [5]
[3] How can an event be alerted? There should be some nodes with long range communication capability to alert there's an event happening. Or by in situ hikers?
1. PSAR and AFNs use their long range radio interface to setup the spatial and temporal coordinate system dynamically; every motes can determine its location with four and more different location informations of PSAR or AFNs broadcast by them; Time for the nodes in the AOI are synchronized at the same time;
2. WSN capabilities discovery: configuration parameters gathering.
3. Setup AOI and call up workforce;
4. A patch of AOI in the WSN is retasked and enter into abnormal event state;
5. Steps 1 to 4 are looped to handle more events; When PSAR and AFNs move to another patch, all the motes in the previous patch returned to normal state;
6. The emergency is handled, all the motes returned to normal state, PSAR and AFNs left the AOI.

# Capability Description
Capability description describes the capabilities of the WSN and its sensors. It can be treated as part of configuration parameters, which must persist through sensor resets, power cycles, reprogramming, and being restored afterward. TinyOS provides an abstraction – Config to handle this situation[6]. Dynamic restasking needs to negotiate with these capabilities.
A WSN has capabilities such as covering size, density of distribution of sensors, types of image, refresh rate and durability, etc. Those strongly correlate with sensors can also be part of sensor's capability.
Table 2: WSN Capability Description
Capability	Description	Example
size	The size of the area that the WSN covers	100 miles^2
density[4]	The distribution density of sensors	3 m^2
Types of image	Number of physical quantities the WSN can provides	Light, humidity
Refresh rate	In normal state, the sampling frequency of every sensor, due to the asynchronism caused by drift of clock of each sensor, this index may be useless for a whole WSN without constant synchronization.	0.1Hz
durability	The time that the WSN can last.	2 years
[4] What about a non-uniform distributed WSN? Average density?

Where does the WSN capability be stored? In a remote command node or in every sensor?
The capability of sensor can be divided into several groups such as computing, sensing, communication, storage and durability. The data for the example in the following table is from “MPR-MIB Users Manual” and “MTS/MDA Sensor Board Users Manual”.
Table 3: Sensor Capability Description
Category	Capability		Description	Example (IRIS XM2110 )
Computing	Processor type		The type of processor, whose architecture determines its instruction set and databus width,etc.	ATMega1281/AVR-8
	With FPU		Integrate with hardware floating point unit?	No
	CPU speed		CPU active frequency and MIPS	7.37MHz/7.37MIPS[7]
	Size of program memory/KB		Size of program memory, mainly on-chip Flash	128
	Size of SRAM/KB		Size of SRAM, mainly on-chip SRAM	8
Sensing/MTS400	Type		Physical quantity	For temperature
	Range		Sensing scope	-40°C to 80°C
	Accuracy		Absolute Accuracy	± 2°C
	Resolution		Total bits of ADC	14
	Response Time		Time for one single complete conversion	5 - 30s
Communication	Chip		Determines its compliance with standard such as IEEE 802.15.4-2003 and performance index	RF230
	Radio Frequency/MHz		Spectrum occupied	2400
	Max. Data Rate/K bits/s		Maximum baud for data transferring	250
	Radio range/m		Open space valid radio range	100
Storage	Chip		Determines page size, read/write/erase time, used for storage of configuration parameters, logging data.	AT45DB014B
	Size/KB		Total volume	512
Durability	Power supply		Power source and capacity	AA, 2×, 2000mA-hr, 3.6 to 2.7 V
	Active power consumption current/mA	CPU		8 @7.37 MHz
		Radio		16@Receive / 17@transmit
		Sensor		5
	Sleep power consumption current/mA	CPU		0.008
		Radio		0.001
		Sensor		0.01

For simple retasking, can be fulfilled by tasking configurable parameters such as sampling frequency, time window (sliding window length for sampling, how many sampling point), digital filtering, average calculation, trend calculation such as speed and acceleration.
Table 4: Task configurable parameters
Category	Parameter	Description	Example
Sampling	Frequency	Number of data points in unit time	0.1 Hz
	Window length	Number of points kept	10
Data processing	Digital filtering
	Average
Trend calculation	Speed
	Acceleration
Alarm	High threshold
	Low threshold
Storage	Linear buffer
	Cycling buffer
	Buffer size

System settings such as parameters for network protocols can also be abstracted to increase system reconfigurability and adaptiveness.

# Implementation
## Rough ideas:
1. Configuration parameters modification by TinyOS ConfigStrorage and its network protocols - dissemination and collection;
2. Script program replacement and injection by TinyOS network protocols - dissemination and collection, which requires a tiny script interpreter to be implemented;
3. Binary application re-imaging by Deluge-T2;
4. Security handled with hardware AES-128 provided by many recent 2.4 GHz ZigBee/IEEE 802.15.4 RF transceiver. Unfortunately, IRIS mote does NOT have so frequency hopping scheme[4] can be used here.

## Program on sensors:
An application on top of TinyOS consists of several TOSThreads:
1. query listening and response thread: listens to the queries from AFNs and responses correspondingly;
2. configuration thread: listens to the requests for reconfigurations from AFNs and carry out correspondingly;
3. normal state task thread: environmental monitoring and event alert
4. exceptional state task thread: handling emergency when be called up as work force by AFNs
5. script interpreting and executing thread: handle script based retasking
6. re-image thread: handle re-image based retasking
7. communication thread: handle network communication
8. storage thread: handle in-network storage
A detailed description will be given with the development of this application.
## Program on AFN (laptop)
The program on AFN communicate with the WSN through USB-Basestation via Serail-Forwarder provided as part of development tools for TinyOS. It carries out following tasks:
1. Query for capabilities of the targeted WSN;
2. Calibrate sensors if needs
3. Call workforce;
4. Retasking the workforce;
5. Get and show informations as images from the workforce;
6. Get and move to a new location in the WSN;
7. Segment by Segment it will draw out a map and a path;
8. Loop through 1 to 5 until campaign accomplished.